AspeedAPB2OPB
Memory region
Size=4K

ast2600 register
Mapped.
OPB memory region Size = 4GB

   FSI Master registers.
   Size = 256 MB
0x80000000
0xa0000000

OPB2FSI region
Size = 256MB
Config space (1K)
CFAM Memory region size = 2MB

Peek Table (1K)
FSI slave register (1K)
0x000
0x400
0x800
0xc00
ScratchPad (1K)
LBUS Memory region
Size = 2MB -0xc00
LBUS engines

- AspeedAPB2OPB has 4K memory region which is mapped to aspeed ast2600 FSI controller registers.
- OPB has 4GB memory
  - Offset 0x80000000 is mapped to FSI master registers. It is 256MB space. This is from the FSI spec.
  - Offset 0xa0000000 is mapped to OPB2FSI. It is 256 MB space.
    - This space is divided into multiple CFAMs. Each CFAM gets 2MB space.
      - CFAM has following sub regions
        - At offset 0 – Config space for CFAM which is 1KB size.
        - At offset 0x400 – Peek table which is 1KB size
        - At offset 0x800 – FSI slave registers which is 1KB size.
        - From offset 0xc00 onwards different engines/devices will be attached to LBUS. Each device get 1KB space.
          - We have only one device which is scratch pad.